## Slide 1: Three Years of Cap Monitoring to Evaluate Remedy Effectiveness in Esquimalt Harbour, BC, Canada
Presented By: Amy Corp, P. Chem, EP, Anchor QEA
Collaborators: Michael Bodman, Department of National Defence
Kristen Ritchot, Public Services and Procurement Canada
Matt Woltman, Derek Ormerod, and Deirdre Reidy, Anchor QEA

## Slide 3
How can we demonstrate cap performance during the initial years following construction?

## Slide 4: Pre-Construction Conditions
Metals, PCBs, and PAH exceedances
  Mercury up to 464 times the screening level
  Phenanthrene up to 235 times the screening level
  Total PCBs up to 109 times the screening level
In surface sediment and down to 3 metres below mudline

## Slide 5: Cap Design
Chemical isolation layer
  Amendments added to reduce cap layer thickness
Armour layer
  Hydrodynamic forces
  Wind and vessel-generated waves
  Vessel-induced propeller wash

## Slide 6: Construction
Conducted January 2019 to May 2020
  48,500 cubic meters dredged
  50,000 cubic meters cap/fill material placed
Shoreline/intertidal area required night work around low-tide windows
Shallow bedrock made dredging and material placement to full thickness challenging in some areas

## Slide 7
Cap model references: Reible 2012; Lampert and Reible 2009; Go et al. 2009; Appendix B of Palermo et al. 1998
Cap Design
Performance Monitoring Sampling Location

## Slide 8
Monitoring Approach
NMDS: nylon mesh diffusion sampler
SPME: solid-phase microextraction

## Slide 9
Nylon Mesh Diffusion Samplers

## Slide 10: SPME Samplers

## Slide 11: Cap Material Testing Results
Similar to baseline pre-placement cap material testing and below regional background levels
No trend observed with depth
Zoomed in
Note: Dashed line represents PEL value.

## Slide 12: Chemical Trends: Mercury
Porewater
Surface Water
Cap Material
Dashed line presents screening criteria where available.

## Slide 13: Chemical Trends: Phenanthrene
Dashed line presents screening criteria where available.
Porewater
Surface Water
Cap Material

## Slide 14: Chemical Trends: PCBs
Dashed line presents screening criteria where available.
Porewater
Surface Water
Cap Material

## Slide 15: Porewater Sampling in Cap Surface: Arsenic
Arsenic in cap similar to surface water and test material concentrations
  Dissolved-phase concentrations appropriate for evaluating cap performance
Total porewater in year 1 much higher than other sample types
  Not indicative of breakthrough
  Potential presence of iron oxide
Note:
Dashed line represents WQG value.

## Slide 16: Elevated Arsenic in Total Porewater Samples
Iron in contact with oxygen produces iron oxide, which is a sink for arsenic
  Visual evidence of orange/brown staining on SPME samplers
Total arsenic in porewater in future years all below water quality guidelines

## Slide 18: Lessons Learned
Cap is performing as expected
  Chemically
  Hydrodynamically
Sampling for multiple media provided greater certainty
Arsenic and sulfide investigations in area

## Slide 19
Amy Corp
Principal Scientist Anchor QEA
acorp@anchorqea.com