## Slide 1: Use of Radiocarbon Data to Evaluate Sources of Carbon Driving Gas Ebullition in Newtown Creek
Presented by: Grace Weatherford, PE, Anchor QEA
Collaborators: Ann McNichol, PhD, Woods Hole Oceanographic Institute; and David Glaser, PhD; Stu Messur; and Amy Corp, Anchor QEA

## Slide 2: Newtown Creek
Dead-end tidal tributary to the East River located between the boroughs of Brooklyn and Queens, New York
Listed on the National Priorities List as a CERCLA (i.e., Superfund) site in 2010
Long history of municipal and private/industrial discharges and releases (such discharges comprise the largest source of freshwater flow)

## Slide 3
Photograph by Bill Rhodes
Photograph by Bill Rhodes
Notes: Add Newtown photo here

## Slide 4: Ebullition
Gas ebullition was evaluated during the Newtown Creek Remedial Investigation/Feasibility Study (RI/FS)
Gas (mostly methane) is formed in sediments by the anaerobic degradation of labile organic carbon (e.g., methanogenesis)
Gas ebullition results when enough gas is formed that it can nucleate to form bubbles, grow, fracture the sediment, and escape to the overlying waterbody
Apparent ebullition at Newtown Creek

## Slide 5
What are the sources of carbon driving ebullition at Newtown Creek?

## Slide 6: Sources of Carbon in Newtown Creek Sediment
Discharges of organic-rich materials (e.g., fecal matter and other anthropogenic organic matter from point source discharges, including combined sewer overflows [CSOs])
Other labile organic contaminants (e.g., unweathered nonaqueous phase liquid [NAPL])
Naturally occurring aquatic vegetation and organisms

## Slide 7: Radiocarbon (Carbon-14)
Carbon-14 (14C) is created in the atmosphere and taken up by living organic matter
  14C in terrestrial organisms mirrors atmospheric 14C‐CO2
  14C in aquatic organisms mirrors 14C‐dissolved inorganic carbon (DIC) in water
When organisms die, interaction with the environment ceases and 14C decays
  Half-life of 14C is 5,730 years
  Material greater than approximately 60,000 years old (fossil or ancient carbon) has no detectable 14C
Carbon Cycle Diagram
Source: University Corporation for Atmospheric Research

## Slide 8
Present-day Carbon-14 Is a Mixture
Sources: Hua et al. 2013; Levin et al. 2010; Weidman and Jones 1993
Note: Radiocarbon content is reported as percent modern carbon (pMC) relative to a standard that represents 1950 atmospheric conditions (pre‑atmospheric nuclear weapons testing)
Pre-bomb Atmospheric 14C
Bomb14C
Present-day
Atmospheric 14C
Present-day
Marine 14C
Pre-bomb Marine 14C

## Slide 9
Flux chambers were installed in locations where ebullition had been observed
Gas samples were collected daily during spring tide events in July and October 2018
Samples were analyzed for 14C-CO2 and 14C- methane (CH4)
In two locations,14C was measured in collocated sediment samples
Newtown Creek Data Collection

## Slide 10
Carbon-14 Results in Sediment Samples
Sediment Samples | 14C - Total C (pMC) 0 to 17.5 cm | 14C - Total C (pMC) >17.5 cm
Arithmetic average | 59 | 40
Range | 47 to 79 | 29 to 53

## Slide 11
Note: 14C in one sample measured 150 pMC. Law et al. attributed this to the release of artificial 14C tracer waste.
Carbon-14 in Discharges
CSO samples collected during the Newtown Creek RI/FS were not analyzed for 14C
Studies (from the literature) conclude that municipal sewage contains a mixture of modern and fossil carbon
  Arithmetic average was calculated from 13 samples collected at 8 facilities between 1998 and 2013
14C-DOC (pMC) | Nara et al. 2010 | Law et al. 2013 | Tseng et al. 2016 | Combined
Arithmetic average | 86 | 90 | 95 | 91
Range | 79 to 92 | 87 to 93 | 76 to 105 | 76 to 105

## Slide 12
Gas Samples | 14C of CH4 (pMC) | 14C of CO2 (pMC)
Arithmetic average | 95 | 94
Range | 84 to 105 | 88 to 98
Carbon-14 Results in Ebullition Gas Samples

## Slide 13
Summary of Carbon-14 Values
Note: Average value shown with vertical bar.
Sources: Hua et al. 2013; Levin et al. 2010; Weidman and Jones 1993; Law et al. 2013; Nara et al. 2010; Tseng et al. 2016

## Slide 14
Carbon that is sequestered from the atmosphere during biomass growth is referred to as “biogenic carbon”
Lewis et al. (2004) provide a method to define the quantitative relationship between pMC and “percent biogenic carbon” for a sample:
Percent biogenic carbon in sample x 100
Approach for Quantifying Biogenic Carbon
Sources: Lewis et al. 2004; Hua et al. 2013; Levin et al. 2010; Weidman and Jones 1993
Carbon Cycle Diagram
Source: University Corporation for Atmospheric Research

## Slide 15
pMC in Newtown Creek ebullition gas samples is 95 (arithmetic average)
pMC of biological material for the past 50 to 100 years is estimated as 105 to 125
Percent biogenic carbon of Newtown Creek ebullition gas is 76% to 90%
Gas Samples | 14C (pMC)
Arithmetic average | 95
Range | 84 to 105
Percent Biogenic Carbon in Ebullition Gas
x 100
x 100
Sources: Lewis et al. 2004; Hua et al. 2013; Levin et al. 2010; Weidman and Jones 1993; Lardie Gaylord et.al. 2019

## Slide 16
Relative Contributions of Carbon Sources to Ebullition in Newtown Creek
Carbon Sources | Contribution
Aquatic organisms Discharges of organic-rich materials (e.g., such as fecal matter from CSOs) | 76% to 90%
Fossil fuels (e.g., petroleum and coal) released in historic spills Discharges containing oils | 10% to 24%

## Slide 17
Ebullition gas generation at Newtown Creek is mainly driven by biogenic sources and, to a lesser extent, fossil carbon.
(Cont..)

## Slide 18
Hua, Q., M. Barbetti, and A. Rakowski, 2013. “Atmospheric Radiocarbon for the Period 1950–2010.” Radiocarbon 55(4).
Lardie Gaylord, M.C., B.E. Longworth, K. Murphy, C. Cobb, and A.P. McNichol, 2019. “Annual Radiocarbon Measurements in a Century-Old European Beech Tree (Fagus sylvatica) from Coastal Northeastern North America.” Nuclear Instruments and Methods in Physics Research Section B: Beam Interactions with Materials and Atoms 456:264–270.
Law, Y., G.E. Jacobsen, A.M. Smith, Z. Yuan, and P. Lant, 2013. “Fossil Organic Carbon in Wastewater and Its Fate in Treatment Plants.” Water Research 47(14):5270–5281.
Levin, I., T. Naegler, B. Kromer, M. Diehl, R.J. Francey, A.J. Gomez-Pelaez, L.P. Steele, D. Wagenbach, R. Weller, and D.E. Worthy, 2010. “Observations and Modelling of the Global Distribution and Long‐Term Trend of Atmospheric 14CO2.” Tellus 62(1):26–46.
Lewis, C.W., G.A. Klouda, and W.D. Ellenson, 2004. “Radiocarbon Measurement of the Biogenic Contribution to Summertime PM-2.5 Ambient Aerosol in Nashville, TN.” Atmospheric Environment 38(35):6053–6061.

## Slide 19
Nara, F.W., A. Imai, K. Matsushige, K. Komatsu, N. Kawasaki, and Y. Shibata, 2010. “Radiocarbon Measurements of Dissolved Organic Carbon in Sewage-Treatment-Plant Effluent and Domestic Sewage.” Nuclear Instruments and Methods in Physics Research Section B: Beam Interactions with Materials and Atoms 268(7–8):1142–1145.
Tseng, L.Y., A.K. Robinson, X. Zhang, X. Xu, J. Southon, A.J. Hamilton, R. Sobhani, M.K. Stenstrom, and D. Rosso, 2016. “Identification of Preferential Paths of Fossil Carbon Within Water Resource Recovery Facilities via Radiocarbon Analysis.” Environmental Science and Technology 50(22):12166–12178.
Weidman, C.R., and G.A. Jones, 1993. “A Shell‐Derived Time History of Bomb 14C on Georges Bank and Its Labrador Sea Implications.” Journal of Geophysical Research 98(C8)14577–14588.

## Slide 20
Grace Weatherford
Senior Managing Environmental Engineer
gweatherford@anchorqea.com
971.409.7313