## Slide 1: Integrating Geostatistical Interpolation Methods and Site Conditions to Define Remedial Action Areas for the Lower Duwamish Waterway Upper Reach
Presented by: Katy Gross, PE, Anchor QEA
Collaborators: John Laplante and Tom Wang, Anchor QEA
Craig Hanson, Windward Environmental, LLC
Jeff Stern and Debra Williston, King County
Allison Crowley; Pete Rude; and Dave Schuchardt, City of Seattle
Joe Flaherty and Ken Nogeire, Boeing

## Slide 2: Project Area
Superfund Site in Seattle, Washington
5-mile-long channelized waterway
Designed and constructed by upper, middle, and lower reaches
Upper Reach from river miles 3.0 to 5.0

## Slide 3: Chemicals of Concern
PCBs
  Account for nearly 90% of contaminated sediment area in the LDW upper reach
  Focus of geostatistical interpolation (indicator kriging) and uncertainty analysis
Other COCs
  Metals, PAHs, SVOCs, dioxins/furans account for ~10% of contaminated area
  Other COCs interpolated separately using simpler method (Thiessen polygons)

## Slide 4: Complex Suite of Remedial Action Levels
Surface Sediment (0–10 cm)
  Remedial Action Level (RAL) for PCBs = 12 mg/kg-OC
Subsurface Sediment (0–45 cm, 0–60 cm)
  RALs for PCBs = 12, 65, or 195 mg/kg-OC, depending on:
    Intertidal vs. subtidal areas
    Shoaling areas in Federal Navigation Channel
    Recovery Categories (natural recovery potential)
Organic carbon-normalization

## Slide 5: Presentative Overview
Interpolation
  Reducing uncertainty in defining areas with RAL exceedances through interpolation methods and phased data collection
Engineering considerations
  Overlaying engineering factors to develop Remedial Action Areas
Start of construction (November 2024) Credit: ldwg.org

## Slide 6
Interpolation

## Slide 7: Selection of Interpolation Method
Methods considered:
  Kriging
    Ordinary
    Indicator
  Inverse Distance Weighting
  Thiessen Polygons

## Slide 8: Selection of Interpolation Method (cont.)
Indicator kriging (IK) selected for PCBs
  Has the advantage of mapping probabilities of RAL exceedances
Thiessen polygons used to interpolate areas of other contaminants with RAL exceedances
PCB indicator kriging probability of RAL exceedance in sediment

## Slide 9: Surface PCB Indicator Probability
W a t e r f r o n t
P a r k
Tar-Like
Material
RAL Exceedance
Probability

## Slide 10: Subsurface PCB Indicator Probability
W a t e r f r o n t
P a r k
Tar-Like
Material
RAL Exceedance
Probability

## Slide 11: Combined PCB Indicator Probability
W a t e r f r o n t
P a r k
Tar-Like
Material
RAL Exceedance
Probability

## Slide 12: Combined PCBs + Other COCs
W a t e r f r o n t
P a r k
Tar-Like
Material
RAL Exceedance Areas
PCBs
(50% Indicator Probability)
Other COCs
(Thiessen Polygons)

## Slide 13: Phased Data Collection
Data collected in three PDI phases to refine geostatistical interpolation after each phase and better identify data gaps to inform subsequent data phases
  Phase I: Define horizontal extents
  Phase II: Refine horizontal extents, vertical data collection, and engineering data
  Phase III: Address design data gaps and increase confidence level

## Slide 15
Engineering Considerations

## Slide 16: Remedial Action Area Development
Geometry
Site physical conditions
Operational and administrative considerations
Review of data interpolation uncertainty
Constructability and recontamination risk minimization

## Slide 17: Development of RAAs: Site Conditions
Geotechnical stability
Offsets from structures, utilities
Historical dredging
Historical dredging bathymetry data from 1958 dredging event by USACE

## Slide 18: Development of RAAs: Operational/Administrative
Cross section with dredge prism compared to early action area dredging as-built
EAAs, Ecology-Led Upland Cleanups, Habitat Areas, ROD Requirements

## Slide 19: Development of RAAs: Interpolation Uncertainty

## Slide 20: Development of RAAs: Constructability and Recontamination Risk Minimization
Area A: Required Dredge Elevation –21.5’ MLLW
Area C: Required Dredge Elevation –21.0’ MLLW
Area D: Required Dredge Elevation –23.0’ MLLW
Area B: Required Dredge Elevation –22.0’ MLLW
Dredge Sideslope

## Slide 21
Geostatistical interpolation is a powerful tool that can be integrated with phased PDI data collection and traditional engineering design considerations to manage uncertainty
Interpolation
  Areas with RAL exceedances = 7.6 acres
Engineering considerations
  Remedial Action Areas = 15.1 acres

## Slide 22
Questions?

## Slide 23
Anchor QEA and Windward, 2022. Pre-Design Investigation Data Evaluation Report for the Lower Duwamish Waterway Upper Reach. Final. Submitted to EPA July 15, 2022.
Anchor QEA and Windward, 2024. 100% Remedial Design Basis of Design Report: Appendix A – Pre-Design Investigation Phase III Data Report for the Lower Duwamish Waterway.
EPA, 2014. Record of Decision. Lower Duwamish Waterway Superfund Site. U.S. Environmental Protection Agency Region 10. November 2014.

## Slide 24
Katy Gross, PE
Managing Engineer
kgross@anchorqea.com