## Slide 1: Modeling Porewater Cleanup Time During Multicomponent Nonaqueous Phase Liquid Dissolution Using a Desorption Approximation
Presented by: Mike Gefell, PG, CPG, Anchor QEA
Collaborators: Ali Meyal, PhD and Deviyani Gurung, PhD, Anchor QEA

## Slide 2
Can we predict porewater concentration decreases due to long-term NAPL dissolution in sediment?

## Slide 3: How Much Will Effective Solubility of Key NAPL Components Decrease In 100+ Years?
Sediment treatment caps designed for extensive periods
Chemical loading may decline due to NAPL weathering
We present a new method to model future concentrations
Coarse-grained sediment visibly saturated with NAPL

## Slide 4: Sediment Cap Design
Typical design assumption for sites with NAPL in sediment
  Porewater loading concentrations remain constant
    But will they really? For 100 years?
Porewater
Flow

## Slide 5: Time 0
Clean Porewater
High Dissolved Concentration for Compound i
NAPL
Sediment
Surface Water or Chemical Isolation Layer

## Slide 6: Time 1
Clean Porewater
High Dissolved Concentration for Compound i
Dissolution
Front

## Slide 7: Time 2
High Dissolved Concentration for Compound i
Clean Porewater
Dissolution
Front

## Slide 8: Time 3
Low Dissolved Concentration for Compound i
Clean Porewater

## Slide 9: Empirical Coal Tar Dissolution Experiment
4.9% NAPL saturation
Source: Eberhardt and Grathwohl 2002

## Slide 10: Dissolved Concentrations Versus Time
In NAPL Zone (MW 1)
Downgradient (MW 2)
VOCs
PAHs
VOCs
PAHs
Water travel time through NAPL zone
≤8 hours
Source: Eberhardt and Grathwohl 2002

## Slide 11: Dissolution Front Retardation
120 pore volume exchanges before naphthalene decreased downgradient
Retardation of dissolution front (Eberhardt and Grathwohl 2002)
Equation 1: R = 1 + (ρ0 fi,o n S0) / (Ci,sat nc)
where:
ρ0 = NAPL density fi,o = mass fraction of compound i in NAPL n = total porosity in NAPL zone S0 = NAPL saturation Ci,sat = effective solubility for compound i nc = effective (water-filled) porosity in the NAPL zone [n(1-S0 )]

## Slide 12: Innovative Solution (Original, Published)
Standard retardation equation for clean-water front during desorption (standard solute-transport modeling)
Equation 2: R = 1 + (ρb/n) Kd
where: ρb = bulk density n = total porosity Kd = distribution coefficient
Equating (1) and (2)
Equation 3: Kd = (ρ0 fi,o n2 S0) / (ρb Ci,sat nc)
Source: Gefell and Gurung 2023a, 2023b

## Slide 13: Numerical Model Setup
1D MT3D model through NAPL zone (1 m long) – 100 cells parallel to flow
Initial dissolved concentration in NAPL zone = Ci,sat
Kd value used in NAPL zone, zero elsewhere (equilibrium partitioning)
Initial sorbed concentration calculated by model
Other parameters from Eberhardt and Grathwohl (2002)
Model Domain

## Slide 14: Model Verification
In NAPL Zone (MW 1)
Downgradient (MW 2)
Indene
Naphthalene
Indene
Naphthalene

## Slide 15: Method Refinement
Modified retardation equation for clean-water front during NAPL dissolution
Equation 2’: R = 1 + (ρb/nc) Kd
where: ρb = bulk density nc = effective (water-filled) porosity in the NAPL zone Kd = distribution coefficient
Equating (1) and (2)
Equation 3’: Kd = (ρ0 fi,o n S0) / (ρb Ci,sat )

## Slide 16: Comparing Published and Refined Methods
Published Method
(Equation 3)
Refined Method
(Equation 3’)

## Slide 17: Model Example: Cap Loading Concentration and Cumulative Mass for Hypothetical Site (100 Years)
NAPL zone in sediment 15 feet (4.6 meters) thick
Mean NAPL saturation 5%, density 1.05 g/cm3, 1% benzene by mass
Effective solubility 10 mg/L
Sediment porosity 0.5, bulk density 1.3 g/cm3
Three comparative simulations
  1 cm/day seepage with aqueous-phase degradation (150-day half life)
  1 cm/day seepage with no degradation
  ISS (no seepage, diffusion dominated transport, no degradation in ISS zone)

## Slide 18: Cap Loading Concentration vs. Time

## Slide 19: Cap Loading – Total Benzene Mass in 100 Years (kg/m2)
Simulations with seepage
  With no concentration change (base case): 3.7
  NAPL weathering without degradation: 1.2 (–66%)
  NAPL weathering with degradation in aqueous phase: 0.80 (–78%)
ISS with NAPL weathering, for comparison: 0.054 (–99%)

## Slide 20: Cap Loading – Total Benzene Mass in 100 Years (kg/m2)
Simulations with seepage
  With no concentration change (base case): 3.7
  NAPL weathering without degradation: 1.2 (–66%)
  NAPL weathering with degradation in aqueous phase: 0.80 (–78%)
ISS with NAPL weathering, for comparison: 0.054 (–99%)
With NAPL weathering, far less benzene loading than base case assumption

## Slide 21: Flow with Degradation (Sensitivity Analysis)
 | Benzene |  | Naphthalene | 
 | Low | High | Low | High
Mass Fraction in NAPL | 0.00500 | 0.02000 | 0.100 | 0.200
NAPL Saturation | 0.01 | 0.15 | 0.01 | 0.15
Seepage Rate (cm/day) | 0.2 | 5 | 0.2 | 5
Degradation Half Life (days) | 100 | 200 | 100 | 200
Notes: For all simulations – porosity = 0.5, effective solubility (both compounds) = 10 mg/L, bulk density = 1.3 g/cm3.
Dispersivity and diffusion coefficients obtained from literature.

## Slide 22: Total Loading Decrease in 100 Years (Percent)
 | Benzene |  | Naphthalene |  | Comments
No concentration change | No change |  | No change |  | 1 cm/day seepage
Sensitivity Analyses |  |  |  |  | 
 | Low | High | Low | High | 
Mass Fraction in NAPL | –88 | –60 | –14 | –7 | 1 cm/day seepage, 150-day half life
NAPL Saturation | –93 | –41 | –4 | –3 | 1 cm/day seepage, 150-day half life
Seepage Rate (cm/day) | –68 | –92 | –9 | –22 | 150-day half life
Degradation Half Life (days) | –82 | –76 | –14 | –7 | 1 cm/day seepage

## Slide 23: Parameter Measurement
Collect samples in zones with most notable NAPL presence
NAPL (from well/piezometer or extract from sediment)
  Density and chemical composition (standard analytical methods)
Bulk sediment
  Standard chemical analysis (if no pure NAPL sample available)
  Dean Stark extraction for NAPL saturation
Porewater
  Exclude NAPL during sampling (e.g., porous ceramic filtration)
  Standard chemical analysis

## Slide 24: Summary
Dissolution of a relatively soluble compound from a complex NAPL can be simulated equivalent to desorption using a calculated Kd value
  Timing of dissolution front
  Concentration decrease over time
Parameters are measurable
Predict porewater quality changes over time
In some cases, can significantly reduce mass and cost of chemical sorbent in cap

## Slide 25
Eberhardt, C., and P. Grathwohl, 2002. “Time Scales of Organic Contaminant Dissolution from Complex Source Zones: Coal Tar Pools vs. Blobs.” Journal of Contaminant Hydrology 59:45–66.
Gefell, M.J., and D. Gurung, 2023. “Modeling Dissolution of Soluble Compounds from Multi-Component NAPL Using a Desorption Approximation.” Groundwater 61(6):879–886.
Gefell, M.J., and D. Gurung, 2023. “Simulating Dissolution of the Most Soluble Compounds from Complex NAPLs Using Equilibrium Partitioning.” Applied NAPL Science Review 11(2).

## Slide 26
Mike Gefell
Principal Scientist
mgefell@anchorqea.com